## Slide 1: Beagle board

## Slide 2: What is beagle board
Introduced on July 28, 2008
A low-power open-source single-board computer
Designed with open source software development in mind

## Slide 3: What is beagle board
designed using Cadence OrCAD for schematics and Cadence Allegro for PCB manufacturing
no simulation software was used

## Slide 4: features
Measures approximately 75mm x 75mm
Has all functionality of a basic computer
Built-in storage and memory provided through a PoP chip
256MB if NAND flash memory & 256MB of RAM
(128MB on earlier models)
Uses upto 2W of power
Can be powered from the USB connector
Separate 5V can also be provided

## Slide 5: Rev. c4 specification
Package on package (PoP) SoC/Memory chip
  Processor TI OMAP3530 SoC – 720 MHz ARM Cortex-A8 core
  "HD capable" TMS320C64x+ core (520 MHz up to 720p @30 fps)
  Imagination Technologies PowerVR SGX 2D/3D graphics processor supporting dual independent displays
  256 MB LPDDR RAM
  256 MB NAND Flash memory

## Slide 6: Rev. c4 specification
Peripheral connections
  DVI-D (HDMI connector chosen for size – maximum resolution is 1280 × 1024 – and it does not output digital audio)
  S-Video
  USB OTG (mini AB)
  1 USB port

## Slide 7: Rev. c4 specification
Peripheral connections
  SD/MMC card slot
  Stereo in and out jacks
  RS-232 port
  JTAG connector
  Power socket (5 V barrel connector type)

## Slide 8: Rev. c4 specification
Development
  Boot code stored in ROM
  Boot from NAND memory, SD/MMC, USB, or serial
  Alternative boot source button.

## Slide 9: Rev. c4 specification
Development
  Has been demonstrated using Android, Angstrom Linux, Fedora, Ubuntu, Gentoo, Arch Linux ARM, openSUSE for ARM and Maemo Linux distributions, VxWorks, FreeBSD, the Windows CE operating system, Symbian, QNX and a version of RISC OS 5 made available by RISC OS Open.

## Slide 10: Use of beagle board
developed by a small team of engineers as an educational board that could be used in colleges around the world to teach open source hardware and software capabilities
to provide users a powerful computer at a low cost with few restrictions
to provide users the open source hardware details so as to continually improve the product line by keeping the line fresh with new innovations.
powerful computing power and small physical size allows them to be used in wide variety of projects